## Slide 1: Development of a computational framework for the prediction of free-ion activities, ionic equilibria and solubility in dairy liquids
Ken Morison & Pariya Noeparvar
Chemical and Process Engineering
University of Canterbury
MADP, September 2017

## Slide 2: Background
When milk, whey, whey permeate or milk protein concentrates are concentrated, calcium phosphate exceeds the solubility limit.
This leads to fouling, and/or changes in the solubility of the dried products.
Fouling from simulated whey

## Slide 3: Aim
To develop a robust method for predicting the state of minerals in milk concentrated by reverse osmosis or evaporation
  To develop a robust method for predicting the state of minerals in solution
  To develop a robust method for predicting precipitation and dissolution dynamics

## Slide 4: Components of the model
The behaviour of mineral in milk depends on their activity, not on concentration. Any good model needs:
Free ion activity coefficients but without 100’s of parameters
Ion-pair equilibria
Solubility
Precipitation and dissolution dynamics
Numerical methods

## Slide 5: Ion Activities
Numerous equations are available.
We require equations suitable for:
  Electrolytes
  Multiple ions (Na+, K+, Ca2+, Mg2+, H+, Cl-, CO32-, PO43-, etc)

## Slide 6: Multiple Ions (Holt, Dalgleish, Jenness, 1981)
Equilibrium association/dissociation constants, Ka are available

## Slide 7: Ion Activities
Numerous equations are available.
We require equations suitable for:
  Electrolytes
  Multiple ions (Na+, K+, Ca2+, Mg2+, H+, Cl-, CO32-, PO43-, etc)
  Free ions and ion pairs (e.g. CaCl+, CaCit- )
  High concentrations (concentrated milk, whey, permeate)
  Lactose (non-electrolyte)

## Slide 8: Ion Activities
Numerous equations are available.
We require equations suitable for:
  Electrolytes
  Multiple ions (Na+, K+, Ca2+, Mg2+, H+, Cl-, CO32-, PO43-, etc)
  Free ions and ion pairs (e.g. CaCl+, CaCit-)
  High concentrations (concentrated milk, whey, permeate)
  Lactose (non-electrolyte)
Options
  Debye-Hückel, Extended Debye-Hückel, Davies, Non-Primitive Mean Spherical Approximation, MSA (Blum), Unrestricted Primitive MSA, etc.

## Slide 9: Davies Equation
Davies Equation
Only applied to charged ions.
All ions of the same charge have the same activity coefficient.
Extended Debye-Hückel
Includes a size term

## Slide 10: Davies Equation
Davies Equation
Only applied to charged ions.
All ions of the same charge have the same activity coefficient.
Extended Debye-Hückel
Includes a size term

## Slide 11: Blum and co-workers: Primitive MSA model
Blum used customary units of his time and place (based on the ESU system). They were never defined in his papers.
ESU units
SI units
His and other papers contained typographical errors.
The resulting equations showed signs of being ill-conditioned.
We couldn’t get them to work!!

## Slide 12: Mean Spherical Approximation Ion Activities
As summarised by van Boekel (2008) from Blum (1975), Mansoori et al. (1970).
Electrostatic and hard sphere terms for ion activity coefficients,
Hard sphere depends on space occupied (from size and number density)

## Slide 13: MSA Ion Activities
As summarised by van Boekel (2008) from Blum (1975), Mansoori et al. (1970).
Electrostatic and hard sphere terms for ion activity coefficients,
Hard sphere (from size and number density)
Important for high concentrations and the contribution of non-electrolytes, e.g., lactose.
Diameter is only fitting parameter for each ion

## Slide 14: MSA Ion Activities
The Bjerrum distance is based on our best estimate of the solution (not solvent) dielectric constant.
Dielectric constant of the solution depends on the solute concentration.

## Slide 15: Numerical Methods
Newton’s method was used to solve ion equilibria equations (up to 100 equations)
Variables were bounded
“Relaxation” (fractional steps) was used
Reasonable initial guesses required
Euler’s method or Heun’s (Modified Euler’s) method was used, with Newton’s method to solve the differential equations for precipitation dynamics.

## Slide 16: Does the model make any difference?
Is the MSA model different from the Davies or Extended Debye-Hückel model?

## Slide 17: Does the model make any difference? Yes
Davies model is inadequate at higher concentrations.
Extended Debye-Hückel is OK
MSA is better but not perfect.
More parameter checking required.

## Slide 18: Does the model make any difference? Yes
Davies model is inadequate at higher concentrations.
Extended Debye-Hückel is OK
MSA is better but not perfect.
More parameter checking required.
Hard Sphere contribution

## Slide 19: Validation
Activities and water activities of NaCl, CaCl2 and H2SO4 solutions 
pH of buffers 
Ion concentration vs pH 

## Slide 20: Validation: Phosphate & Citrate Buffers
http://www.sigmaaldrich.com/life-science/core-bioreagents/biological-buffers/learning-center/buffer-reference-center.html
Na2HPO4 + NaH2PO4 and Na3Citrate + Citric acid

## Slide 21: Phosphate equilibria
Model from Rice et al. Int Dairy J (2010) Current work

## Slide 22: Phosphate equilibria
Model from Rice et al. Int Dairy J (2010) Current work

## Slide 23: With adjustments to Ka of CaPO4- and CaHPO4
Model from Rice et al. Int Dairy J (2010) Current work

## Slide 24: Difficulties
The literature values of association constants, Ka, and solubility products, Ksp, are based on Davies or Extended Debye-Hückel activity models.
New values of Ka and Ksp should be determined for the MSA activity.
Will Ka and Ksp be constant at high concentration?

## Slide 25: Precipitation and dissolution models
In chemistry classes precipitation is fast.
In the Ca-H-PO4 system precipitation is slow (minutes to days).
Example

## Slide 26: Precipitation and dissolution models
Define saturation, , and supersaturation, , for electrolyte using activities, and .
The rate of precipitation, possible equation
Dissolution, possible equation

## Slide 27: Validation: Precipitation of CaHPO4
Based on Arifuzzaman & Rohani (2004). NaOH added over time to CaCl2 & NaH2PO4 (0.6 mmol/L Ca and P).
, k =0.18 min-1, n =2
Original Ka, Ksp. Only k was fitted
Saturation of DCPD (dicalcium phosphate dihydrate

## Slide 28: Validation: modelled as DCPA to DCPD
Mekmene et al. (2009). Time response after mixing CaCl2, NaH2PO4 and NaOH.
20 mmol/L PO4
Ca:P 1, 1.5, 2.0
Some fitting of Ksp and k values was required
Dicalcium phosphate anhydrous precipitates quickly then redissolves to form dehydrate?

## Slide 29: Many Different Solubility Products
Octacalciumphosphate (OCP) Ca8(HPO4)2(PO4)4
{ } indicates activity.
Authors | Ion Activity Product, IP | Ksp
Tung et al. Rice et al. (2010) |  | 
Driessens and Verbeeck (1990) |  | 
Authors | Ion Activity Product, IP | Ksp
Tung et al. Rice et al. (2010) |  | 
Driessens and Verbeeck (1990) |  | 

## Slide 30: Milk
Many cations, anions and ion-pairs
Lactose
Simulate ions concentration of
  Serum minerals
  Serum + lactose = whey permeate

## Slide 31: Lactose activity
Lactose is a non-electrolyte so is not included in the Debye Hückel or Davies equations.
It is included as a hard sphere term in the MSA theory.
Lactose is assumed to be the same as sucrose.
The activity coefficient is sufficiently well approximated by hard sphere term with an effective molecule diameter of 0.49 nm.

## Slide 32: Lactose activity
Lactose is a non-electrolyte so is not included in the Debye Hückel or Davies equations.
It is included as a hard sphere term in the MSA theory.
Lactose is assumed to be the same as sucrose.
The activity coefficient is sufficiently well approximated by hard sphere term with an effective molecule diameter of 0.49 nm.

## Slide 33: Effect of lactose during concentration
Milk minerals
No lactose
Milk minerals
+ lactose
X indicates normal concentration in milk

## Slide 34: Effect of lactose during concentration
Milk minerals
No lactose
Milk minerals
+ lactose
X indicates normal concentration in milk

## Slide 35
Lactose has a significant effect on saturation of calcium phosphate when whey permeate is concentrated to 50% solids
Effect of lactose during concentration
Milk minerals
No lactose
Milk minerals
+ lactose

## Slide 36
Lactose has a significant effect on saturation of calcium phosphate when whey permeate is concentrated to 50% solids
Effect of lactose during concentration
DCPD
Milk minerals
No lactose
Milk minerals
+ lactose

## Slide 37
The Davies equation is very different.
The Extended Debye-Hückel equation is better but with no lactose effect.
Effect of lactose during concentration
Davies Equation
Extended Debye-Hückel

## Slide 38: Next steps
Add casein to the model system to simulate milk
Dynamics of precipitation in milk systems
  Ca-H-PO4 precipitation with lactose: experimental and predicted
  Does viscosity affect precipitation?
Uncertainty of Ksp, Ka, at high concentration
Find the limitations of this approach

## Slide 39: Conclusions
The ion equilibria of milk-like systems were modelled and solved using:
  MSA activity model
  Newton’s method
The Davies equation is not as good at higher concentrations.
Extended Debye-Hückel does include lactose effect.
Dynamic precipitation was successfully added using Heun’s method (modified Euler).